ZXA10 C320 V1.2.5P2T6 Version Upgrade Guide

File Number：

Version Number：A

Prepared by / Date

Approved by / Date

Contents

1.	Version Description	3

2.	Version Upgrade/Roll back	3

2.1.	Upgrade Preparation	3

2.1.1.	Tools	3

2.1.2.	Hardware	3

2.1.3.	Software preparation, data backup and running status checking and recording	3

2.1.4.	Configuration checking before version upgrade	4

2.2.	Upgrade Operation Procedures	4

2.2.1.	Set up the environment	4

2.2.2.	Running the FTP Server	4

2.2.3.	Configure the NE	4

2.2.4.	Download and Synchronize the Version	7

2.2.5.	Version Upgrade	10

2.2.6.	Confirm the version upgrade success	11

2.2.7.	CPLD upgrade	11

2.3.	Rolling back the Version	13

2.3.1.	Criterion of whether to roll back the version	13

2.3.2.	The method of rolling back the version	13

3.	Testing for the upgrade	13

4.	Notes	13

4.1.	The Compatibility Issues of C320 V1.2.0 T5 Upgrading to C320 V1.2.0P1T2	13

4.2.	The Compatibility Issues of C320 V1.2.0 P1T2 rolling back to C320 V1.2.0T5	14

5.	The versions which to be upgraded need to be coincident	14

6.	Checklist	15

Scope of Application：ZTE engineers who operate the version upgrading, and the engineers of the partners or customers. These engineers must be familiar with principles and hardware structure of C320, debugging and maintaining C320 skillfully.

# Version Description

This version is the 6th test version of ZXA10 C320 V1.2.5P2.

# Version Upgrade/Roll back

## Upgrade Preparation

### Tools

Generally, we need a Laptop, a serial cable and a RJ-45 cable. Furthermore if needing to burn the BOOT chip off-line, please prepare a chip extractor and a burner.

### Hardware

Another control board and PON card are required for backup

### Software preparation, data backup and running status checking and recording

Upgrading the version to C320 V1.2.5T6, we do not need to clear the configurations, but we should take care of the command compatibility of new version. After downloading new version, it is highly recommended connecting main control board with your computer through serial cable and then restarting C320. Please observe the rebooting process carefully. If any error message is printed on the screen during the period of loading configuration, please modify the corresponding command configuration when the system works.

The .boot, .mvr and .fw version files of all cards are required to be updated. And the steps of upgrade are shown as following:

- Prepare all the version files of all cards.

- Backup the configuration data file startrun.dat to the server as following:

ZXAN#upload cfg startrun.dat  //upload the configuration file to the specified FTP server。

Uploading file to host(12.1.2.26)

Uploading file startrun.dat ...

........[Successfully]

(Pre-conditions：set the external ftp server or the ftp server of NMS).

- Upload the running version files to the FTP server in either of the following ways

- a. Right-click the NE icon in NM, select 【system management】－>【version management】, upload the current saved version files of all cards to ftp server which is online,(such as control boards, PON cards and uplink cards)

- b. telnet to NE with CLI, upload img, for example:

ZXAN#upload img *   //upload all the version files to specified FTP server

Uploading file to host(12.1.2.26)

Uploading file etgo.fw ...

..........[Successfully]

Uploading file etgo.mvr ...

................

Pre-conditions：set the external ftp server or the ftp server of NMS.

- Check and record the running status before upgrading, check whether there are alarms with NE or not: select the NM menu【View】( 【Alarm Management】 to check the NE alarm. If there are alarms, please resolve the alarm problem before upgrading the version.

### Configuration checking before version upgrade

- Write the configurations.

- Check whether the uplink ports are separated or aggregated and make sure the separated uplink ports have different PVIDs.

- The VLANs bound to uplink ports in tagged mode can be displayed normally in case of blocking after OLT reboot.

- The uplink ports need to be in enforced full duplex mode(except special situations).

- Collect the version information on current network.

- Collect the information of type, version, uplink mode, connecting requirements (if the version of uplinked equipments is relative with OLT version) of uplinked equipments. If there is any incompatibility, a pretreatment plan is needed.

- Collect the information of type, version and compatibilities of down-linked equipments. If there is any incompatibility, a pretreatment plan is needed.

- Collect the information of version and compatibilities of NM. If there is any incompatibility, the NM version needs upgrading first.

## Upgrade Operation Procedures

### Set up the environment

In the way of CLI upgrading, you need a FTP server and the version files used for upgrading. The FTP server must be connected to the OLT successfully.

Figure 1 Upgrade with CLI mean

### Running the FTP Server

Run the FTP server，configure the FTP username and password, put the version files into the specified path.

### Configure the NE

- After the C320 system starting is completed, command show interface mng1 is used to get the information about out-band MAC，IP，ftp server IP，username, password, etc.

ZXAN#show interface mng1

mng running information

ip address      : 12.1.2.103

mask            : 255.255.255.0

boot-server     : 12.1.2.26

boot-username   : test

boot-password   : ******

config-filename : startrun.dat

imgfile-location: local

inband-mac      : 00d0.d012.2318

outband-mac     : 00d0.d012.2319

Note：

Ip address : the out-band IP address.

In the mng1 interface, you can modify the out-band IP address, FTP server IP address and the user name and password consistent with the FTP server.

ZXAN(config)#interface mng1                     ；Enter the mng1 interface mode

ZXAN(config-if)#ip address 12.1.2.103 255.255.255.0  ；Modify the out-band IP address

ZXAN(config-if)#boot-server 12.1.2.26              ；Modify IP address of ftp server ZXAN(config-if)#boot-username test                ；Modify username of ftp server

ZXAN(config-if)#boot-password test                ；Modify password of ftp server

The command of the mng1 interface:

ZXAN(config-if)#?

boot-password     FTP password for boot server

boot-server       Specify remote boot server

boot-username     FTP username for boot server

config-filename   Start config file name

default-gateway   Default gateway for boot file download

enable-password   Password for enable entrance

end               Exit to EXEC mode

exit              Exit current configuration mode

imgfile-location  Bootup imaging file location

ip                Configure ip address

no                Negate a command or set its defaults

show              Show running system information

shutdown          Shutdown port

Note：The in-band/out-band MAC address can be modified in boot mode. The method of entering the boot mode: restart the NE,the serial port will print: Press ENTER key to stop auto-boot...，you will enter the boot mode if you press enter in 3 seconds time.

ZXAN#reboot

Confirm to reboot? [yes/no]:y

ZXAN#####

Board name    : SMXA

SubCard name  : UCDC/1

Boot version  : V1.2.0T3

Creation date : 2012-06-06 14:08:02

Pcb version   : 110701

Cpld version  : V1.3

Serial number :

Attached TCP/IP interface to mottsec1.

Attaching network interface lo0... done.

Mounting file system /flash ...

done.

Mounting file system /log ... done.

IsMaster.txt file read success

init bootp cfg ok

Press ENTER key to stop auto-boot...

3

[SMXA]/flash/img/>p

Boot Location [0:Net,1:Flash] : 1

Client IP                     : 12.1.2.103

Netmask                       : 255.255.255.0

Server IP                     : 12.1.2.26

Gateway IP                    :

FTP User                      : test

FTP Password                  :

Inband MAC address            : 00-d0-d0-12-23-18

Outband MAC address           : 00-d0-d0-12-23-19

Boot Config File              : startrun.dat

[SMXA]/flash/img/>c

'.' = clear field;  '-' = go to previous field;  ^D = quit

Boot Location [0:Net,1:Flash] : 1

Client IP                     : 12.1.2.103

Netmask                       : 255.255.255.0

Server IP                     : 12.1.2.26

Gateway IP                    :

FTP User                      : test

FTP Password                  :

Inband MAC address            : 00-d0-d0-12-23-18

Outband MAC address           : 00-d0-d0-12-23-19

Boot Config File              : startrun.dat

### Download and Synchronize the Version

Note：Before upgrading the version, you must update the boot version first !

Step 1 download the version to master control board

After the system started, in the privilege mode (ZXAN#),use command download img ***(file name) to download the version files. The new version files should contain .bt, .fw and .mvr version files according to the line cards of the NE, including MSP.MVR and all corresponding patch files.

For example：

ZXAN#download img smxa.bt

Downloading from host(12.1.2.26)

Transfering file smxa.bt ...

.......................[Successfully]

Synchronizing file smxa.bt to slave board...

........................................[Successfully] //if slave control board is not existed or the status of slave control board is not “standby”, the version file will not be synchronized to the slave control board automatically.

ZXAN#download img smxa.fw

Downloading from host(12.1.2.26)

Transfering file SMXA.FW ...

...........[Successfully]

Synchronizing file SMXA.FW to slave board...

....................[Successfully]  //if slave control board is not existed or the status of slave control board is not “standby”, the version file will not be synchronized to the slave control board automatically.

ZXAN#download img smxa.mvr

Downloading from host(12.1.2.26)

Transfering file SMXA.MVR ...

...................................................................................[Successfully]

Synchronizing file SMXA.MVR to slave board...

...........................................................................................[Successfully]    //if slave control board is not existed or the status of slave control board is not “standby”, the version file will not be synchronized to the slave control board automatically.…… ……

Tips：You can use wildcard to download the version so as to improve the efficiency of the downloading. Such as command download img  *  //download all the version files in ftp server to the flash of NE（In the procedure of the downloading, when the CLI is full screen and appear the more prompt, you may press spacebar to continue）.

Step 2 Synchronize the version files to the slave control board. When the version files have been downloaded to the master control board, if the slave control board is in standby status, the version will be synchronized automatically. But if the slave control board is plugged after the version download or the control board is not in standby status, you may need to use command to synchronize the image files to it. In the privilege mode(ZXAN#), command sync-file img is provided to synchronize the version files from master control board to slave control board. For example：

ZXAN#sync-file img

command ZXAN#show sync-status is provided correspondingly to check the progress of the synchronization. For example：

ZXAN#sho sync-status

Synchronization status of directory /flash/img/ :

Filename                            Status

--------------------------------------------------------------------------------

bsp.mvr                             100

gtghg.bt                            100

gtghg.fw                            100

gtghg.mvr                           100

gtgoe.bt                            100

gtgoe.fw                            100

gtgoe.mvr                           100

gtgog.bt                            100

gtgog.fw                            100

gtgog.mvr                           100

pm.fw                               100

smxa.fw                             100

smxa1.mvr                           100

smxa.bt                             100

14 files sync OK, Total 14 files

Step 3 Confirm that the synchronization between master and slave control boards is successful. After the synchronization between the master control board and the slave control board，use the command show version-saved（master/slave），to check whether the version files are the same or not between these two boards.

ZXAN#show version-saved master

PhyLoc FileName    VerType VerTag            BuildTime           Length   Active

--------------------------------------------------------------------------------

1/1/4  bsp.mvr     MVR     v1.0              2012-09-27 10:16:13 1212669

1/1/4  gtghg.bt    BT      V4.0.0            2013-01-30 16:54:16 524288

1/1/4  gtghg.fw    FW      V1.2.5P2          2013-09-23 01:14:49 78842

1/1/4  gtghg.mvr   MVR     V1.2.5P2          2013-09-23 01:14:48 4939176

1/1/4  gtgoe.bt    BT      V1.2.0P1          2012-10-24 14:17:00 387020

1/1/4  gtgoe.fw    FW      V1.2.5P2          2013-09-23 01:52:53 4298811

1/1/4  gtgoe.mvr   MVR     V1.2.5P2          2013-09-23 01:52:53 1886523

1/1/4  gtgog.bt    BT      V4.0.0            2013-03-05 14:11:46 524288

1/1/4  gtgog.fw    FW      V1.2.5P2          2013-09-23 02:11:58 59946

1/1/4  gtgog.mvr   MVR     V1.2.5P2          2013-09-23 02:11:57 5193224

1/1/4  etgo.fw     FW      V1.2.5P2          2013-09-21 23:25:49 1427718

1/1/4  etgo.mvr    MVR     V1.2.5P2          2013-09-21 23:25:48 5009999

1/1/4  etgod.bt    BT      V1.2.0            2012-06-14 15:52:36 249604

1/1/4  pm.fw       FW      V1.2.5P2          2013-09-22 22:22:22 934

1/1/4  smxa.bt     BT      V4.0.0            2013-09-13  9:34:23 524288

1/1/4  smxa.fw     FW      V1.2.5P2          2013-09-23 07:34:25 492068

1/1/4  smxa0.mvr   MVR     V1.2.5P2          2013-09-12 07:02:00 13984601 0

1/1/4  smxa1.mvr   MVR     V1.2.5P2          2013-09-23 07:34:16 13989282 1

ZXAN#show version-saved slave

PhyLoc FileName    VerType VerTag            BuildTime           Length   Active

--------------------------------------------------------------------------------

1/1/3  bsp.mvr     MVR     v1.0              2012-09-27 10:16:13 1212669

1/1/3  gtghg.bt    BT      V4.0.0            2013-01-30 16:54:16 524288

1/1/3  gtghg.fw    FW      V1.2.5P2          2013-09-23 01:14:49 78842

1/1/3  gtghg.mvr   MVR     V1.2.5P2          2013-09-23 01:14:48 4939176

1/1/3  gtgoe.bt    BT      V1.2.0P1          2012-10-24 14:17:00 387020

1/1/3  gtgoe.fw    FW      V1.2.5P2          2013-09-23 01:52:53 4298811

1/1/3  gtgoe.mvr   MVR     V1.2.5P2          2013-09-23 01:52:53 1886523

1/1/3  gtgog.bt    BT      V4.0.0            2013-03-05 14:11:46 524288

1/1/3  gtgog.fw    FW      V1.2.5P2          2013-09-23 02:11:58 59946

1/1/3  gtgog.mvr   MVR     V1.2.5P2          2013-09-23 02:11:57 5193224

1/1/3  etgo.fw     FW      V1.2.5P2          2013-09-21 23:25:49 1427718

1/1/3  etgo.mvr    MVR     V1.2.5P2          2013-09-21 23:25:48 5009999

1/1/3  etgod.bt    BT      V1.2.0            2012-06-14 15:52:36 249604

1/1/3  pm.fw       FW      V1.2.5P2          2013-09-22 22:22:22 934

1/1/3  smxa.bt     BT      V4.0.0            2013-09-13  9:34:23 524288

1/1/3  smxa.fw     FW      V1.2.5P2          2013-09-23 07:34:25 492068

1/1/3  smxa0.mvr   MVR     V1.2.5P2          2013-09-23 07:34:16 13989282 1

1/1/3  smxa1.mvr   MVR     V1.2.5P2          2013-09-12 07:02:00 13984601 0

### Version Upgrade

- Use the command show card to check the status of the line card，and to confirm which slots need to be upgraded.

ZXAN#show card

Rack Shelf Slot CfgType RealType Port    HardVer SoftVer         Status

-------------------------------------------------------------------------------

1    1     1    ETGO    ETGOD    8       091201  V1.2.5P2        INSERVICE

1    1     2    GTGO    GTGOE    8       110301  V1.2.5P2        INSERVICE

1    1     3    SMXA    SMXA     N/A     110701  V1.2.5P2        STANDBY

1    1     4    SMXA    SMXA     N/A     110702  V1.2.5P2        INSERVICE

- Use the command show version-running to check the running version, and to verify the boot version is upgraded successfully.

ZXAN#show version-running

PhyLoc  FileType   VerType    VerTag            BuildTime           VerLength

--------------------------------------------------------------------------------

1/1/1   ETGO       MVR        V1.2.5P2          2013-08-27 23:36:54 5008113

1/1/1   ETGOD      BT         V1.2.0            2012-06-14 15:52:36 249604

1/1/3   SMXA       MVR        V1.2.5P2          2013-08-28 07:15:09 13982546

1/1/3   SMXA       BT         V4.0.0            2013-08-12 12:00:21 524288

1/1/4   SMXA       MVR        V1.2.5P2          2013-08-28 07:15:09 13982546

1/1/4   SMXA       BT         V4.0.0            2013-08-12 12:00:21 524288

1/1/2   GTGOE      MVR        V1.2.5P2          2013-08-28 01:59:52 1886472

1/1/2   GTGOE      FW         V1.2.5P2          2013-08-28 01:59:53 4298811

1/1/2   GTGOE      BT         V1.2.0P1          2012-10-24 14:17:00 387020

- Use the command update-boot slotno [slotno id] to upgrade the boot version

ZXAN#update-boot slotno 1

......................................................................................................................................................................................................................[Successfully]

ZXAN#update-boot slotno 2

......................................................................................................................................................................................................................[Successfully]

ZXAN#update-boot slotno 3

.................................................................[Successfully]

ZXAN#update-boot slotno 4

...........................................[Successfully]

- Reboot the NE

After upgrading the version and saving configuration, reboot the NE.

ZXAN#write

Building configuration...

..[OK]

ZXAN#reboot

Confirm to reboot? [yes/no]:y

### Confirm the version upgrade success

After the NE restarted successfully, you need to check whether the upgrading is successful.

- Use the command show version-running to verify that all of the running versions of the line cards are the same as the versions which we want to upgrade.

For example：

ZXAN#show version-running

PhyLoc  FileType   VerType    VerTag            BuildTime           VerLength

--------------------------------------------------------------------------------

1/1/1   ETGO       MVR        V1.2.5P2          2013-09-21 23:25:48 5009999

1/1/1   PM         FW         V1.2.5P2          2013-09-22 22:22:22 934

1/1/1   ETGOD      BT         V1.2.0            2012-06-14 15:52:36 249604

1/1/2   GTGOE      FW         V1.2.5P2          2013-09-23 01:52:53 4298811

1/1/2   PM         FW         V1.2.5P2          2013-09-22 22:22:22 934

1/1/2   GTGOE      MVR        V1.2.5P2          2013-09-23 01:52:53 1886523

1/1/2   GTGOE      BT         V1.2.0P1          2012-10-24 14:17:00 387020

1/1/3   SMXA       MVR        V1.2.5P2          2013-09-23 07:34:16 13989282

1/1/3   SMXA       BT         V4.0.0            2013-09-13  9:34:23 524288

1/1/4   SMXA       MVR        V1.2.5P2          2013-09-23 07:34:16 13989282

1/1/4   SMXA       BT         V4.0.0            2013-09-13  9:34:23 524288

If CPLD is not required to be upgraded, the version upgrading is finished. And then, please check all the services according to Section 6.

If CPLD has to be upgraded, please follow Section 2.2.7.

### CPLD upgrade

The methods to upgrade the cpld version as below:

- Confirm the .fw file has been downloaded to the main control board.

- Use the command show updatecpld to check the upgrade status of CPLD.

ZXAN#show updatecpld

Rack   Shelf   Slot   RealType   NextResetUpdate   LastUpdateResult   Version

-----------------------------------------------------------------------------

1      1       1      ETGOD      NO                SUCCESS            V1.5

1      1       2      GTGOE      NO                SUCCESS            V2.2

1      1       3      SMXA       NO                SUCCESS            V1.6

1      1       4      SMXA       NO                SUCCESS            V1.6

- Use command update-cpld to set the CPLD upgrade flag.

ZXAN#update-cpld slotno 1 swtval 1

%Code 35670: Cpld update flag is set successfully.

- Use command show updatecpld to check whether the CPLD update is set successfully or not.

ZXAN#show updatecpld

Rack   Shelf   Slot   RealType   NextResetUpdate   LastUpdateResult   Version

-----------------------------------------------------------------------------

1      1       1      ETGOD      YES               SUCCESS            V1.5

1      1       2      GTGOE      NO                SUCCESS            V2.2

1      1       3      SMXA       NO                SUCCESS            V1.6

1      1       4      SMXA       NO                SUCCESS            V1.6

“NextResetUpdate” flag is set as “YES”, which means cpld upgrade is set successfully. For example, all the cards mentioned above will upgrade the CPLD version when the cards are rebooted.

- Reset cards except master control board to upgrade the CPLD version

Reset the cards except master control board to upgrade the CPLD version. When the line card status is “inservice”，and the slave control card is in “standby” status，you can continue the next operation.

Note：in this step, you cannot reset the master control board

Command as below:

ZXAN#reset-card slotno 1

Confirm to reset card? [yes/no]:y

- Save the configurations and restart the NE

ZXAN#write

Building configuration...

..[OK]

ZXAN#reboot

Confirm to reboot? [yes/no]:y

PS: The NE will swap automatically when the Master Control Card cpld upgrade is in processing.

- Use command show update-cpld to check whether the cpld version is upgraded successfully or not.

ZXAN#show updatecpld

Rack   Shelf   Slot   RealType   NextResetUpdate   LastUpdateResult   Version

-----------------------------------------------------------------------------

1      1       1      ETGOD      NO                SUCCESS            V1.5

1      1       2      GTGOE      NO                SUCCESS            V2.2

1      1       3      SMXA       NO                SUCCESS            V1.6

1      1       4      SMXA       NO                SUCCESS            V1.6

- Reboot the OLT to upgrade the CPLD version of  master control boards

PS:

  - All the result of “Show” Command listed here is only used to specify the steps of upgrading, which may be different with the official released version. For more detail information of official released version, please refer to “Specification of Released Version”.

  - The detailed CPLD Version listed here may be different with the official released version. The CPLD version of official released version will be listed in “Specification of Released Version”

## Rolling back the Version

### Criterion of whether to roll back the version

If you cannot finish the version upgrade or there is one or more major failures within a specified time, you must roll back the version.

### The method of rolling back the version

The method of rolling back version is the same as the method of upgrading the version. Please refer to the “Upgrade Operation Procedures” in this document.

# Testing for the upgrade

Service Testing：Check whether the customer services are normal, such as Internet, IPTV, VOIP of ONU.

NM testing：Check that the NM connection is normal, the NM can synchronize and configure the data, and the alarm can appear in NMS

# Notes

About upgrading the NE:  the .boot, .mvr and .fw version files of the cards must be coincident; And all of the three files of the online line cards must be downloaded to the control board, otherwise the line cards may not start appropriately after the upgrade.

## The Compatibility Issues of C320 V1.2.0 T5 Upgrading to C320 V1.2.0P1T2

- During the process of loading configuration, C320 will report error messages about adding some ONUs to the receive-port of IGMP, which is printed as following:

Execute cmd line 21730 error:'igmp  mvlan 3911 receive-port gpon-onu_1/1/2:1 vport 1'

But the multicast service seems not be effected by this error message. The ONU configured as “receive-port” of certain MVLAN is able to join the groups of this MVLAN successfully.

## The Compatibility Issues of C320 V1.2.0 Upgrading to C320 V1.2.5T4

- If some cards that are not supported by V1.2.0, such as GTGHG and etc., have to be used in V1.2.5, please update the whole system to V1.2.5 first, and then plug these cards. Or else, certian task of main control card will be suspended.

## The Compatibility Issues of C320 V1.2.0 P1T2 rolling back to C320 V1.2.0T5

- During the process of loading configuration, C320 will report error messages about adding smartgroup interface to the receive-port of IGMP, which is printed as following:

Execute cmd line 22217 error:'igmp  mvlan 3942 receive-port smartgroup1'

The reason is that the range of “receive-port” is extended in Version P1T2, in which that smartgroup interface can be configured as receive-port directly. But in version T5, IGMP receive-port is not able to accept any smartgroup interface. So, in version T5, in order to achieve the similar effect of P1T2, we have to add all the member interface of smartgroup to the receive-port of IGMP manually.

- In version T5, if system is rebooted, it is possible that the status of ETGOF will maintain “HWONLINE”. Please unplug and plug ETGOF, when the status of master / slave control card is changed to “inservice/standby”.

## The Compatibility Issues of C320 V1.2.5T4 rolling back to C320 V1.2.0

- If some cards that are not supported by V1.2.0, such as GTGHG and etc., is used or configured in V1.2.5, please unplug these cards, and then restore the configuration to V1.2.0. Or else, certian task of main control card will be suspended.

# The versions which to be upgraded need to be coincident

The hardware version of NE：

The coordinate version of NMS: NetNumenU31R20V12.13.40T02, it is strongly recommended that if any problem found during the usage please confirm whether there are newly released NM version or patches.

The coordinate version of uplinked equipment: no requirement.

The coordinate version of ONT: please refer to the newest distribution list of related ONT.

# Checklist

1) The internet service is normal or not

2) The IPTV service is normal or not

3) The VOIP service which is in the same PON interface is normal or not

4) The VOIP service which is in different PON interfaces is normal or not

5) The VOIP service which call to PSTN is normal or not

6) The communication between the master and standby control board is normal or not

7) Switching from the master control board to the slave is normal or not

8) The communication between the NE and the NM is normal or not

9) The NM command can be executed normally or not

10) The new alarms can appear in NMS or not.

# Text boxes

FTP Server

GPON OLT

GPON OLT

GPON OLT

operator